The tender texts below comprise the most common solutions in practice so that options and parts that are not required can be deleted and only quantities need to be inserted.

For certain projects it is recommended to edit the texts. Our experienced colleagues will be pleased to support you competently, quick and free of charge when it comes to create your tender texts. Please contact us via sales@nivus.com or by phone: +49 7262 9191-794.

NivuFlow Mobile 600

Mains-independent portable flow rate measurement

with extremely long battery life, built-in data logger

and GPRS modem for remote data transmission, limit

value alerting and device diagnostics, suitable for use

and programming in Ex zone 1.

Measurement of homogeneous, clear to slightly

polluted media in full pipes and rectangular profiles.

Detection of average flow velocities in up to 2 measurement

paths simultaneously based on the transit time difference

principle.

Universal system use for wet and contactless (clamp-on)

measurement with one transmitter only

Flow measurement transmitter with integrated numeric

discharge models to detect the average flow velocity

from up to 2 individual acoustic paths.

Calculation of the real flow profile by integrating

all measured path velocities covering the wetted cross-

sectional area

Flow rate calculation from average flow velocity and

channel shape considering the medium temperature

and channel dimensions based on internal numeric

discharge models.

Programming, representation of readings and data
transmission via secured, password-protected WLAN

connection without the need to open the instrument.

Programming options using the separate display and 
operating module Type ZAB 01 or via standard

smartphones, tablets or laptop using Android, Windows

or iOS operating systems.

Internal storage and transmission of all relevant

measurement data.

Delay-free and event-based detection of measurement

values including switchover of measurement cycles,

programmable via digital input, flow velocity, flow rate,

water temperature or analog input as limit value threshold

Flow rate, flow velocity or medium temperature can be

put out continuously on free scalable analog output.

Output of free programmable volume impulses, event-

related messages or limit values via digital output.

Integrated alarm management when falling below /

exceeding limit values and automated additional

data transmission to the NIVUS Web Portal,

triggered by flow rate, average flow velocity,

medium temperature and battery voltage as well as

for analog inputs 1 and 2.

5 free programmable high and low limit values

per measurement channel (Q, v, T, AE1, AE2).

5 free programmable low limit values for the

battery voltage

Reset of limit value violation through automated

retransmission of data, programmable by using

the hysteresis settings per measurement channel.

Direct message and automated data transmission

via digital input.

Automatic error message in case of sensor

interruption.

Rugged, shock-proof, absolutely water-tight compact

plastic enclosure suitable for use in wastewater.

Redundant power supply thanks to 2 easily replaceable

gas-tight rechargeable batteries with double plug-in

connection.

Options for additional external power supply with

plug power adapter, solar panel, fuel cell, extra

batteries or similar.

Integrated LED for easy visual identification of

instrument status and error messages without the need to

open the transmitter.

Modern, intuitive operation using external touchscreen.

Automatic sensor detection and indication of

article number, serial number and sensor type.

System reconciliation to increase the measurement

accuracy through automatic reading of calibrated

sensor-specific parameters.

Programming with flat hierarchical structure, supported

by colours and graphic elements, visual true-to-scale

representation of shapes and sensor positions in order to

avoid errors during commissioning.

Error diagnostics related to time and sensor.

Integrated recorder function with min. and max. memory.

Storage of all path velocities, average flow velocities,

flow rates and medium temperature in internal high 
capacity memory.

Up to 3 external analog signals such as levels, overflow

volumes, reference readings etc. as well as one digital

input (counter, run time) can be saved additionally.

Programming data and all saved readings as well errors

as can be read out via WLAN or USB stick.

Protection:	IP 68 (closed)

IP 67 (cover open)

Ex protection	Zone 1 (optional)

Power supply:	1/2 replaceable rechargeable lead gel

batteries, 12 V DC/14 Ah each

Battery life:	up to 19 months without replacement

Internal data	up to 182 000 data sets

memory:

Max. memory	20 years with 1h cycle

period:

Measuring modes:	- cyclic
- continuous
- cyclic switching over to
  continuous based on event
- varying cycle times with switchover
   based on event

Storage interval:	intervals separately adjustable for

normal and event-based operation
Interval cycles:	5, 10, 15, 20 and 30 seconds
	1, 3, 5, 10, 15, 20, 30 and 60
	minutes

Data transmission:	via WLAN, USB stick or
internal GPRS modem (optional)

remote data transmission to available

NIVUS Web Portal

Inputs:	1 or 2 sensor pairs transit time principle

2 x 0/4-20 mA (active)

1x 0/4-20 mA (passive)

1x digital input (active)

1x power adapter/alternative 
power supply

Outputs: 	1x voltage output 0-10 V

1x digital output (SPDT)

1x USB-A interface fur USB stick

Connection:	using waterproof and non-corrosive

IP 68 plug connectors.

Integrated automatic sensor detection

including article no., serial no. and

sensor-specific parameters

Material:	glass fibre reinforced plastic

Weight:	approx. 2.2 kg (without battery)

Versions:	NFM-0600 000 (no Ex,

no internal GPRS modem)

NFM-0600 G0E (no Ex,

with internal GPRS modem)

NFM-0600 0EE (Ex,

no internal GPRS modem)

NFM-0600 GEE (Ex,

with internal GPRS modem)

Transmitter incl. memory stick, activation magnet

and screw driver to open the battery compartment.

Deliver including plugged NIVUS multi-roaming SIM card

with 1 year of free data transmission to the NIVUS

WebPortal (only for versions with internal

GPRS modem, optional).

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Data transmission fee for the NIVUS devices Type

NFM with integrated LTE modem and NLG.

Required tariff after the free 12-month data transmission

included with the purchase of a new NFM or NLG

has expired.

Transmission of readings to the NIVUS WebPortal

or via NIVUS data kiosk to a customer system.

Shortest permissibe

measurement cycle:	1 minute

Shortest permissibe

transmission cycle:	1 hour

Period of notice:	3 months to the end of the

contract period

Total contract

period:	……… years

Version:	SNI0CONNECT01

Unlock for the device in use

Type: ............................

Make: .....................

Qty.:  1 	EP: ..................

GP: ....................

Licence Key

For device -related transmission of measurement 
data using a customer SIM card.

Transmission via FTP and/or e-mail to customer

server or free selectable e-mail address.

Provision of access data for NFM unlocking by

operator.

Version:	NFM0 LIZENZ FTP

Provision of access data by e-mail

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Gas-tight rechargeable battery with built-in double

plug-in connection for quick battery replacement.

Designed for long-term optimised power supply
of the portable NFM 600 transmitter.

Type:	lead gel

Voltage:	12 V DC

Capacity:	14 Ah

Weight:	approx. 4.0 kg

Version:	NFM0 ZAPB 1215

Deliver

Type:............................

Make:.....................

Qty.:  2 Pcs.	UP: ..................

TP: ....................

Power adapter with charging tray for rechargeable

battery Type NFM0 ZAPB 1215 and as extra

power supply for NFM.

Version:	NFM0 ZLAD

Deliver

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Display and operating module for NFM series

IP67-certified 8" outdoor tablet

Resolution:	1280 x 800

Operation:	touchscreen

Operating system:	Android

Communication:	WLAN, USB, Bluetooth,
2G, 3G and 4G.

Version:	NFM0 ZAB0 1

Deliver and install ready to use

Type:............................

Make:.....................

Qty:  1 Pc.	UP: ..................

TP: ....................

Sensor pair for installation on full pipes from the

outside (no medium contact) for DN 80 to

DN 2500.

Measurement through pipe walls made of various

materials.

Detection of flow velocities by 2 ultrasonic

sensors per used acoustic measurement path.

Installation using tensioning belt or rail mounting

system (optional).

Meas. ranges:	- 10 m/s to 10 m/s

Meas. frequency:	1 MHz

Meas. uncertainty:	0.125 % of velocity detection in
	measurement path

Materials:	stainless steel 1.4571 (AISI 316 Ti); 
PEEK

Protection:	IP 68

Cable length:	7 m (option: 10/15/20/30/50 m)

Cable connection:	integrated plug for NFM

Version:	NIC CO 01

Deliver and install ready to use according to

manufacturer specifications

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Tensioning system
for fastening of 2 clamp-on sensors,

consisting of 8 mm tensioning belt, 2 turnbuckles

and 1 tube of special coupling paste

Belt material:	1.4301 (AISI 304)

Length:	10 m, can be split

Operating

temperature:	- 45°C to 200 °C

Coupling paste qty.:	75 g

Version:	ZUB0SPSYS08

Deliver

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Mounting system with movable sensor seats

as variable fixture and for easy adjustment and 
maintenance of acoustic measurement paths
with clamp-on method.

Suitable for 2 pcs. of Type NIC CO01 sensors 
for installation on pipes.

Slide rails with scale to determine sensor distance

and for sensor adjustment.

Incl. fastening material for easy installation on

various pipe diameters.

Incl. special coupling paste for acoustic coupling

of ultrasonic clamp-on sensors.

Material:	Aluminium

Fastening:	up to DN 1000 with tensioning belt

Options:	up to DN 2000 with tensioning belt

up to DN 3000 with tensioning belt

up to DN 3000 with metal tape

Version:	ZUB CO RA 001

Deliver and install ready to use according to

manufacturer specifications

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

Flow-optimised, wet flow velocity sensor pair
without internal electronic components for

installation in full pipes through the pipe wall

for DN 80 to DN 2500.

Sensor pair with integrated stop ball valves,

welding nozzles, special cable and configured

common plug for direct connection to NFM 600.

Detection of flow velocities by 2 ultrasonic
sensors per used acoustic measurement path.

Installation through welding nozzle with
1“ screw-in thread.

Meas. ranges:	- 20 m/s to 20 m/s

Measurement	0.125 % of velocity detection

uncertainty:	within measurement path (v)

Max. operating

pressure:	16 Bar

Materials:	stainless steel 1.4571 (AISI 316 Ti); PEEK

Tube length:	300 mm

Protection:	IP 68

Cable length:	10 m (option: 15/20/30/50/100 m)

Cable connection:	integrated plug for NFM

Version:	TSP0 V200 RL0

Deliver and install ready to use according to

manufacturer specifications

Type:............................

Make:.....................

Qty.:  1 Pair	UP: ..................

TP: ....................

Intrinsically safe T-shape antenna for remote data

transmission with fixed cable and water-tight

IP 68 plug for direct connection to NFM 750.

Protection:	IP 68

Ex-Protection:	Ex ib for zone 1

Cable length:	2.5 m with integrated plug for

connection to NFM

Version:	NFM0 ZANT 1

Deliver, install and connect ready to use according

to manufacturer specifications

Type: ............................

Make: .....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Instructions on handling, installation, setting of

parameters and data evaluation of NFM 600 under

real measurement place conditions

(if available and provided).

Duration:	4 hours

Qty.:  Flat Rate	UP: xxxxxxxxxxx

TP: ....................

Accessories

Wall thickness measurement system for accurate

determination of unknown material thickness on

various pipes.

Battery-powered handheld unit incl. pluggable

sensor.

Version:	NBM0 TG

Deliver

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

NFM suspension device for fastening

on step irons

Material:	stainless steel 1.4571 (AISI 316 Ti)

Version:	NFM0 ZHAK NFM0 2

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

NFM suspension device for fastening

on step irons incl. 2 integrated suspension brackets

for coiled sensor cables.

Material:	stainless steel 1.4571 (AISI 316 Ti)

Version:	NFM0 ZHAK NFM0 1

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Brackets for mechanical protection of NFM connection

plugs in harsh environments such as shafts, canals,

industrial plants etc.

Suitable for additional fastening of a Connector Box

Type NFM0 ZVS1.

Material:	stainless steel 1.4571 (AISI 316 Ti)

Version:	NFM0 ZSBL IRE

Deliver incl. fastening material and install on NFM

ready to use

Type:............................

Make:.....................

Qty.:  1 Pair	UP: ..................

TP: ....................

Connector Box for parallel connection of multiple

input and output signals to NFM

Material:	plastic

Protection:	IP 67

Cable length:	0.2 m

Cable connection:	configured plug

Version:	NFM0 ZVS1

Deliver

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Pre-configured cable with plug and open

cable ends for direct connection of inputs and

outputs to NFM without Connector Box

Plug protection:	IP67

Cable length:	10 m

Cable connection:	one side with pre-configured plug
	one side with open cable ends

Versions:	NFM0 ZVER AEA for active
analog input

NFM0 ZVER AEP for passive
analog input

NFM0 ZVER AA for analog 
output

NFM0 ZVER DE for digital 
input

NFM0 ZVER DA for digital 
output

NFM0 ZVER MU for all inputs
and outputs

Deliver

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Pre-configured cable with plug and open

cable ends for alternative external NFM

power supply via solar panel, fuel cell,

external batteries, rechargeable batteries etc.

Plug protection:	IP67

Cable length:	5 m

Cable connection:	one side with pre-configured plug
	one side with open cable ends

Version:	NFM0 ZVER PS

Deliver

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

WEB Portal

Data remote transmission software

Device-related access for the web-based NIVUS

data collection system.

Data collection system with centralised data storage

and device communication.

Devices connecting with centre save readings and

status data in a centralised data bank.

Data security and availability according to current

IP security standards.

Transmitted readings are provided in the portal for

1 year and can be downloaded manually.

Device overview and device status are available in

the portal. Measurement spots can be localised on an

integrated map. Readings are saved in the data bank

using the recording frequency and can be recalled

by using an Internet browser.

The http server can be operated with any Internet browser

available on the market.

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: part of the transmitter standard delivery